## Slide 1
Model parameters (1 of 4): geometry and mass
Variable | Value | Units
m1 - Feed mass | 6.5 | kg
r_feed - Feed body radius | 0.10 | m
h_feed - Feed body length | 0.20 | m
z_feed - Feed centre height above vertex | 1.01 | m
r_ring - Feed strut ring radius | 0.10 | m
r_dish - Dish rim radius | 1.0 | m
f_dish - Dish focal length | 0.91 | m
thick_dish - Dish shell thickness | 0.0127 | m
rho_dish - Dish effective density | 1050 | kg/m^3
z_rim - Dish rim height above vertex | 0.275 | m
m_hub - Hub mass | 45 | kg
r_hub - Hub radius | 0.10 | m
h_hub - Hub depth | 0.20 | m
z_hub - Hub centre height | -0.10 | m
m_sh - Derived shell mass | about 45 | kg
m2 - Derived dish plus hub mass | about 90 | kg
Source: Parameters section of feed_jitter_controls.mlx. Derived values are calculated from the listed inputs; placeholders need real data.

## Slide 2
Model parameters (2 of 4): struts and joints
Variable | Value | Units
n_truss - Struts number of struts | 3 | -
N_el - Struts beam elements per strut | 4 | -
m_truss - Struts mass of one strut | 1.5 | kg
d_o - Struts tube outer diameter | 0.05 | m
t_wall - Struts tube wall thickness | 2 | mm
nu_poisson - Struts poisson ratio | 0.33 | -
E_ref - Struts young's modulus (aluminium) | 69 | GPa
L_truss - Struts strut length | 1.16 | m
k_nom - Struts reference axial stiffness | 1.8 x 10^7 | N/m
k_joint_ax - Joints axial stiffness | 5 x 10^7 | N/m
k_joint_lat - Joints lateral stiffness | 2 x 10^7 | N/m
k_joint_rot - Joints rotational stiffness | 1 x 10^4 | N m/rad
Source: Parameters section of feed_jitter_controls.mlx. Derived values are calculated from the listed inputs; placeholders need real data.

## Slide 3
Model parameters (3 of 4): base, damping and wind
Variable | Value | Units
k_base - Base translational stiffness | 9.75 x 10^8 | N/m
k_base_rot - Base rotational stiffness | 8.1 x 10^8 | N m/rad
e_base - Base pivot distance behind vertex | 0.30 | m
zeta - Damping modal damping ratio | 0.02 | -
rho_air - Wind air density | 1.225 | kg/m^3
U_mean - Wind mean wind speed | 15 | m/s
I_u - Wind turbulence intensity | 0.25 | -
L_u - Wind integral length scale | 30 | m
Cd_feed - Wind feed drag coefficient | 1.0 | -
A_feed - Wind feed frontal area | 0.04 | m^2
C_N - Wind dish normal-force coefficient | 1.2 | -
C_S - Wind dish side-force coefficient | 0.3 | -
C_M - Wind dish aero moment coefficient | 0.10 | -
A_dish - Wind dish aperture area | 3.14 | m^2
z_cp - Wind centre of pressure height | 0.137 | m
Source: Parameters section of feed_jitter_controls.mlx. Derived values are calculated from the listed inputs; placeholders need real data.

## Slide 4
Model parameters (4 of 4): optics and analysis settings
Variable | Value | Units
f / D - Optics focal ratio | 0.455 | -
k_B - Optics beam deviation constant | 0.45 | -
BDF - Optics beam deviation factor | 0.87 | -
c_tilt - Optics feed-tilt effect on LOS | 0 | -
rf_Hz - Optics operating frequency | 225 | GHz
HPBW - Optics half-power beamwidth | 0.80 | mrad
HPBW / 10 - Optics pointing budget | 80 | urad
T_expo - Analysis exposure time | 600 | s
elev_deg - Analysis elevation angles | 30, 45, 60, 90 | deg
k_vals - Analysis strut stiffness sweep | 10^6 to 10^9 | N/m
f_band - Analysis frequency band | 0.1 to 1000 | Hz
Source: Parameters section of feed_jitter_controls.mlx. Derived values are calculated from the listed inputs; placeholders need real data.